## Slide 1: BCAAIML Computer Networks BCAAIML 403
Sonali Mondal
Assistant Professor CSIT
Kalinga University
Naya Raipur (C.G.), India
PLEASE LEAVE THIS SPACE BLANK

## Slide 2: COURSE OBJECTIVES
Please remember the following text:-
To help students understand the network architecture, including hardware and software technologies, and to provide basic knowledge of data communication.-
To help students understand how networks work in terms of layered architecture, including a set of protocols and their implementation.-
To help students understand the practical aspects of Ethernet working based on IEEE standards.-
To help students understand the general principles of networking, including routing algorithms, Internet architecture, and addressing. Please remember the following text:-
To help students understand the network architecture, including hardware and software technologies, and to provide basic knowledge of data communication.-
To help students understand how networks work in terms of layered architecture, including a set of protocols and their implementation.-
To help students understand the practical aspects of Ethernet working based on IEEE standards.- To help students understand the general principles of networking, including routing algorithms, Internet architecture, and addressing.

## Slide 3: COURSE OUTCOMES
The students will be able to understand the structure and organisation of computer networks, including the division into layers, the role of each layer, and the relationships between the layers.
The students will have a basic understanding of Communication techniques and the functioning of the physical layer.
The students will be able to understand the basic concepts of data link layer properties, including the flow control mechanisms.

## Slide 4: CONTENTS
CLASS NAME MCA | 
Semester-IV | 
Paper Code – BCAAIML | 
SUBJECT NAME- Computer Network | 
S.No. | Unit-1
1 | Introduction
2 | Seven Layers of OSI Model
3 | Layer -7 to Layer 1
4 | Data Encapsulation
5 | OSI Model Analogy
6 | TCP/IP Model
7 | Transmission Media

## Slide 5: REFERENCES/TEXT BOOKS
Text Books:
1. A.S. Tanenbaum " Computer Network: Second Ed. Prentice Hall, India(tan)
2. B.A. Frouzan, Data Communication, Tata McGraw Hill.
Reference Books:
1. D. Berekas and R. Gallager, " Data Networks", second Ed. Prentice Hall, India
2. D.E. Coner," Internetworking with TCP/IP", Vol-I. Prentice Hall India.

## Slide 6: LECTURE PLAN
Lecture No. | Topics to be covered | Slide No.
L-1 | Introduction | 8-9
L-2-4 | Seven Layers of OSI Model | 10-14
L-5 | Layer -7 to Layer 1 | 15-27
L-6 | Data Encapsulation | 28-29
L-7-8 | OSI Model Analogy | 30-44
L-9 | TCP/IP Model | 45-64
L-10 | Transmission Media | 65-66
Quiz |  | 67-76

## Slide 7: UNIT 1

## Slide 8
The Open Systems Interconnection Basic Reference Model (OSI Reference Model or OSI Model) is an abstract description for layered communications and computer network protocol design. It was developed as part of the Open Systems Interconnection (OSI) initiative. In its most basic form, it divides network architecture into seven layers.
It is therefore often referred to as the OSI Seven Layer Model. Open Systems Interconnection (OSI) is a set of internationally recognized, non-proprietary standards for networking and for operating systems involved in networking functions.
8

## Slide 9
To address the problem of networks increasing in size and in number, the International Organization for Standardization (ISO) researched many network schemes and recognized that there was a need to create a network model
This would help network builders implement networks that could communicate and work together
ISO therefore, Introduced the OSI reference model in 1978 and revised it in 1984.
9

## Slide 10
Session
Physical
10
Transport
Network
Data Link
Presentation
Application
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1

## Slide 11
11

## Slide 12: OSI Model's 7 Layers
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
Application to Application
Application to Application
Application to Application
Process to Process
Hop to Hop
Switch
Hop to Hop
Physical Medium
Hub and Repeater
Router
Source to Destination
Source to Destination
12

## Slide 13
Supports the communication between applications over the network
Presents data to the receiver in a form it recognises
Establishes a connection and terminates it when no longer required
Acknowledges the flow of data including re-transmission where required
Adds the appropriate network addresses to packets
Adds the MAC addresses to packets
Transmits the data on the medium
NODE A
Sending Device
NODE B
Receiving Device
Layer 7
Application Layer
Layer 6
Presentation Layer
Layer 5
Session Layer
Layer 4
Transport Layer
Layer 3
Network Layer
Layer 2
Data Link Layer
Layer 1
Physical Layer
Layer 7
Application Layer
Layer 6
Presentation Layer
Layer 5
Session Layer
Layer 4
Transport Layer
Layer 3
Network Layer
Layer 2
Data Link Layer
Layer 1
Physical Layer
13

## Slide 14: Application (Upper) Layers
Data Flow Layers
14
Application
Presentation
Session
Transport
Network
Data-Link
Physical

## Slide 15
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
The top layer of the OSI model
Provides a set of interfaces for sending and receiving applications to gain access to and use network services. Processing.
deal with applications.
This layer networking Examples:
Email
Web browsers
15

## Slide 16
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
This layer is responsible for presenting the data in the required format which may include:
Code Formatting/Translation
Encryption
Compression
16

## Slide 17
Manages data-format information for networked communications (the network’s translator).
For outgoing messages, it converts data into a generic format for network transmission; for incoming messages, it converts data from the generic network format to a format that the receiving application can understand.
This layer is also responsible for certain protocol conversions, data encryption/decryption, or data compression/decompression.
A special software facility called a “redirector” operates at this layer to determine if a request is network related or not and forwards network-related requests to an appropriate network resource.
17

## Slide 18
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
This layer establishes, manages, and terminates sessions between two communicating hosts.
Creates Virtual Circuit
Coordinates communication between systems
Organize their communication by offering three different modes
  Simplex
  Half Duplex
  Full Duplex
18

## Slide 19:  Enables two networked resources to hold ongoing communications (called a session) across a network
Applications on either end of the session are able to exchange data for the duration of the session
This layer is:
  Responsible for initiating, maintaining and terminating sessions
  Responsible for security and access control to session information (via session participant identification)
  Responsible for synchronization services, and for checkpoint services

## Slide 20
14
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
This layer breaks up the data from the sending host and then reassembles it in the receiver.
It provides reliable data
transport network.
Other
across the
features of this
layer are:
Sequencing
Acknowledgment
Retransmission
Flow Control

## Slide 21
Manages the transmission of data across a network
Manages the flow of data between parties by segmenting long data streams into smaller data chunks (based on allowed “packet” size for a given transmission medium)
Reassembles chunks into their original sequence at the receiving end
Provides acknowledgements of successful transmissions and requests resends for packets which arrive with errors

## Slide 22
16
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
End to End Delivery
Provide logical addressing that routers use for path determination
Internetwork Communication
Packet forwarding
Packet Filtering
Makes “Best Path Determination”

## Slide 23
Handles addressing messages for delivery, as well as translating logical network addresses and names into their physical counterparts
Responsible for deciding how to route transmissions between computers
This layer also handles the decisions needed to get data from one point to the next point along a network path
This layer also handles packet switching and network congestion control

## Slide 24
Preamble | DMAC | SMAC | Data length | DATA | FCS
18
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
Performs Physical Addressing
This layer provides reliable transit of data across a physical link.
Access to media using MAC address
Error detection
LLC and MAC
Logical Link Control performs Link establishment
MAC Performs Access method

## Slide 25
Handles special data frames (packets) between the Network layer and the Physical layer
At the receiving end, this layer packages raw data from the physical layer into data frames for delivery to the Network layer
At the sending end this layer handles conversion of data into raw formats that can be handled by the Physical Layer

## Slide 26
20
7 | Application
6 | Presentation
5 | Session
4 | Transport
3 | Network
2 | Data Link
1 | Physical
This is the physical media through which the data, represented as electronic signals, is sent from the source host to the destination host.
Move bits between devices
Encoding

## Slide 27
Converts bits into electronic signals for outgoing messages.
Converts electronic signals into bits for incoming messages.
This layer manages the interface between the computer and the network medium (coax, twisted pair, etc.)
This layer tells the driver software for the MAU (media attachment unit, ex. network interface cards (NICs, modems, etc.)) what needs to be sent across the medium.
The bottom layer of the OSI model.

## Slide 28
Data-Link
Physical
Network
Upper-Layer Data
Upper-Layer Data
TCP Header
Data
IP Header
Data
LLC Header
0101110101001000010
MAC Header Data
Application
Presentation
Session
Transport
Segment
Packet
Bits
Frame
PDU
FCS
FCS

## Slide 30
After riding your new bicycle a few times in Bangalore, you decide that you want to give it to a friend who lives in Delhi.

## Slide 31
Make sure you have the proper directions to disassemble and reassemble the bicycle.

## Slide 32
Call your friend and make sure you have his correct address.

## Slide 33: Disassemble the bicycle and put different pieces in different boxes. The boxes are labeled “1 of 3”, “2 of 3”, and “3 of 3”.

## Slide 34: Put your friend's complete mailing address (and yours) on each box.Since the packages are too big for your mailbox (and since you don’t have enough stamps) you determine that you need to go to the post office.
2
8

## Slide 35
Bangalore post office takes possession of the boxes.

## Slide 36
The boxes are flown from Bangalore to Delhi.

## Slide 37
Delhi post office receives your boxes.

## Slide 38: Upon examining the destination address, Delhi post office determines that your boxes should be delivered to your written home address.

## Slide 39
Your friend calls you and tells you he got all 3 boxes and he is having another friend named BOB reassemble the bicycle.

## Slide 40: Your friend hangs up because he is done talking to you.

## Slide 41: BOB is finished and “presents” the bicycle to your friend. Another way to say it is that your friend is finally getting him “present”.

## Slide 42
Your friend enjoys riding his new bicycle in Delhi

## Slide 44: Although the OSI reference model is universally recognized, the historical and technical open standard of the Internet is Transmission Control Protocol / Internet Protocol (TCP/IP).
The TCP/IP reference model and the TCP/IP protocol stack make data communication possible between any two computers, anywhere in the world, at nearly the speed of light.
The U.S. Department of Defense (DoD) created the TCP/IP reference model because it wanted a network that could survive any conditions, even a nuclear war.

## Slide 45
Process / Application Layer
Host-to-Host Layer
Internet Layer
Network Access Layer

## Slide 46: Process/Application Layer
The Process layer contains protocols that implements user level functions such as mail delivery, file transfer and remote login. This layer is actually the combination of upper three layers of OSI model i.e. Application, Presentation and Session.
Host-to Host Layer
The Host-to Host layer handles connection assignation, flow control, retransmission of lost data, and other generic data flow management.

## Slide 47: Internet Layer
The Internet layer is responsible for delivering data across a series of different physical networks that interconnect a source and destination machine.
Routing protocols are most closely associated with
this layer, as is the IP Protocol, the internet’s
fundamental protocol.
Network Access Layer
The Network Access layer is responsible for delivering data over the particular hardware media in use.
Different protocols are selected from this layer,
depending on the type of physical network.

## Slide 49
45
Source Port (16) |  |  | Destination Port (16)
Sequence Number (32) |  |  | 
Acknowledgment Number (32) |  |  | 
Header Length (4) | Reserved (6) | Code Bits (6) | Window (16)
Checksum (16) |  |  | Urgent (16)
Options (0 or 32 if Any) |  |  | 
Data (Varies) |  |  | 
20
Bytes
Bit 0
Bit 15
Bit 16
Bit 31

## Slide 50: F T S D T S T E M N F N P L T S T M N P P P E T
46
TCP
Port Numbers
Transport
Layer
UDP
Application
Layer
21
23
25
53
69
161
R I P
520

## Slide 51
Source
Port
Destination
Port
…
Host A
1028 23 …
SP
DP
Host Z
Telnet Z
Destination port = 23. Send packet to my Telnet
application.

## Slide 52: Windowing in networking means the quantity of data segments which is measured in bytes that a machine can transmit/send on the network without receiving an acknowledgement.

## Slide 54
Another function of the transport layer is to provide optional flow control.
Flow control is used to ensure that networking devices don’t send too much information to the destination, overflowing its receiving buffer space, and causing it to drop the sent information
The purpose of flow control is to ensure the destination doesn't get overrun by too much information sent by the source

## Slide 55
User Datagram Protocol (UDP) is the connectionless
transport protocol in the TCP/IP protocol stack.
UDP is a simple protocol that exchanges datagrams, without acknowledgments or guaranteed delivery. Error processing and retransmission must be handled by higher layer protocols.
UDP is designed for applications that do not need to put sequences of segments together.
The protocols that use UDP include:
  TFTP (Trivial File Transfer Protocol)
  SNMP (Simple Network Management Protocol)
  DHCP (Dynamic Host Control Protocol)
  DNS (Domain Name System)

## Slide 56
 No sequence or acknowledgment fields
54
Source Port (16) | Destination Port (16)
Length (16) | Checksum (16)
Data (if Any) | 
1
Bit 0
Bit 15
Bit 16
Bit 31
8
Bytes

## Slide 57
1
Bit 0
Bit 15 Bit 16
Bit 31
Version (4) | Header Length (4) | Priority &Type of Service (8) | Total Length (16) | 
Identification (16) |  |  | Flags (3) | Fragment Offset (13)
Time-to-Live (8) |  | Protocol (8) | Header Checksum (16) | 
Source IP Address (32) |  |  |  | 
Destination IP Address (32) |  |  |  | 
Options (0 or 32 if Any) |  |  |  | 
Data (Varies if Any) |  |  |  | 
20
Bytes

## Slide 58: Transport Layer
 Determines destination upper-layer protocol
57
Internet Layer
TCP
UDP
Protocol Numbers
IP
17
6

## Slide 59
58
Application
Internet
Data-Link
Physical
Destination Unreachable
Echo (Ping) Other
Transport
1
ICMP

## Slide 60
 Map IP
 Local ARP
MAC
172.16.3.1
IP: 172.16.3.2
Ethernet: 0800.0020.1111
172.16.3.2
IP: 172.16.3.2 = ???
I heard that broadcast. The message is for me. Here is my Ethernet
address.
I need the Ethernet address of 176.16.3.2.
60

## Slide 61: I heard that broadcast. Your IP address is 172.16.3.25.
 Map MAC
IP
Ethernet: 0800.0020.1111
IP: 172.16.3.25
Ethernet: 0800.0020.1111 IP = ???
What is my IP
address?
61

## Slide 62
61

## Slide 63
It is a logical construct that identifies a specific process or a type of service.
A port is always associated with an IP address of a host and
the protocol type of the communication, and thus completes the
destination or origination address of a communications session.
well known ports registered ports
private or dynamic ports
0-1023
1024-49151
49152-65535
Common TCP/UDP ports
53-DNS
161-SNMP
531-AOL INSTANT MESSENGER WELL KNOWN PORTS
21-FTP,23-TELNET,25-SMTP,80-HTTP,110-POP3,194-IRC,443-SECURE HTTP
REGISTERED PORTS
1863-MSN MESSENGER,2000-CISCO SCCP,8008-ALTERNATE HTTP,8080-ALTERNATE HTTP

## Slide 64
OSI(Open System Interconnection) | TCP/IP(Transmission Control Protocol / Internet Protocol)
1. OSI provides layer functioning and also defines functions of all the layers. | 1. TCP/IP model is more based on protocols and protocols are not flexible with other layers.
2. In OSI model the transport layer guarantees the delivery of packets | 2. In TCP/IP model the transport layer does not guarantees delivery of packets.
3. Follows horizontal approach | 3. Follows vertical approach.
4. OSI model has a separate presentation layer | 4. TCP/IP does not have a separate presentation layer
5. OSI is a general model. | 5. TCP/IP model cannot be used in any other application.
6. Network layer of OSI model provide both connection oriented and connectionless service. | 6. The Network layer in TCP/IP model provides connectionless service.
7. OSI model has a problem of fitting the protocols in the model | 7. TCP/IP model does not fit any protocol
8. Protocols are hidden in OSI model and are easily replaced as the technology changes. | 8. In TCP/IP replacing protocol is not easy.
9. OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them. | 9. In TCP/IP it is not clearly separated its services, interfaces and protocols.
10. It has 7 layers | 10. It has 4 layers

## Slide 65: Transmission Media

## Slide 66: Interconnection Devices
Router
Gateways
Bridges
Hubs

## Slide 67: Multiple Choice Questions
1 OSI stands for __________
Open System Interconnection Operating System Interface Optical Service Implementation Open Service Internet
2. The number of layers in ISO OSI reference model is __________ 4 5 6 7

## Slide 68: Multiple Choice Questions
3.TCP/IP model does not have ______ layer but OSI model have this layer. Session Layer Transport Layer Application Layer Network Layer
4. Which layer is used to link the network support layers and user support layers? Session Layer Data Link Layer Transport Layer Network Layer

## Slide 69: Multiple Choice Questions
5.Which address is used on the internet for employing the TCP/IP protocols? Physical Address And Logical Address Port Address Specific Address All Of The Mentioned
6. TCP/IP model was developed _____ the OSI model. Prior To After Simultaneous To With No Link To

## Slide 70: Multiple Choice Questions
7. Which layer is responsible for process to process delivery in a general network model? Network Layer Transport Layer Session Layer Data Link Layer
8. Which address is used to identify a process on a host by the transport layer? Physical Address Logical Address Port Address Specific Address

## Slide 71: Multiple Choice Questions
9. Which layer provides the services to user? Application Layer Session Layer Presentation Layer
None of the above
10. Transmission data rate is decided by ____________ Network Layer Physical Layer Data Link Layer Transport Layer

## Slide 72: Multiple Choice Questions
11. The sharing of a medium and its link by two or more devices is called _________ Fully duplexing Multiplexing Micropleixng Duplexing
12.Multiplexing is used in _______ Packet switching Circuit switching Data switching Packet & Circuit switching

## Slide 73: Multiple Choice Questions
13.Which multiplexing technique used to transmit digital signals? FDM TDM WDM FDM & WDM
14.Multiplexing provides _________ Efficiency Privacy Anti jamming Both Efficiency & Privacy

## Slide 74: Multiple Choice Questions
15. In TDM, slots are further divided into _________ Seconds Frames Packets Bits
16.The ground station in VSAT communication is called
Hub
HTTP
Multiplexer
Repeater

## Slide 75: Multiple Choice Questions
17.____ units) in a single bus structure communicate at a time.
One
Two
Three
Four
18.Where does bridge operate in OSI model?
Application layer
Data link layer
Physical layer
Both a and b

## Slide 76: Multiple Choice Questions
19.Encryption and Decryption are the functions of ___ layers.
Transport
Session
Presentation
Physical
20.Which layer 4 protocol is used for a Telnet connection?
TCP
IP
UDP
TCP/IP